mrDiffusion Simulator
tech report

Introduction
Why another diffusion simulator?
Who made it?
Etc.

Theory
We estimate the number of water molecules in a voxel of brain tissue by first assuming the voxel is full of water (this is roughly true?). Then, the number of molecules (n) can be easily estimated as:
n = AN * density * volume / MolecularWeight
where AN is Avogadro's number= 6.022*1023 atoms/mole. Density*volume is simply mass-: 1cm^3 of water at 37deg is about 0.9933 (e.g., see http://en.wikipedia.org/wiki/Specific_gravity and http://www.engineeringtoolbox.com/water-density-specific-weight-d_595.html). The molecular weight of water is computed from its atomic composition: 1O+2H = 16+2 = 18. Thus, a 2mm^2 voxel of pure water at body temperature contains 6.022*10^23*0.9933*0.2^3/18 = 2.6585e+20 water molecules. More relevant for MR imaging, the voxel contains twice this many 'spins' (Hydrogen nuclei). Thus, our voxel contains roughly 5.3e+20 spins.
At room temperature, only a small fraction of the spins in a voxel produce an MR signal. These correspond to the lower energy spins that outnumber the higher energy spins. (Boltzmann statistics- see http://www.cis.rit.edu/htbooks/mri/chap-3/chap-3.htm.)
n-/n+ = e-E/kT
E is the energy difference between the spin states; k is Boltzmann's constant, 1.3805x10-23 J/Kelvin; and T is the temperature in Kelvin (body temperature is 310.15 K). In practice, E<<kT, so the above can be simplified to:
n- - n+ = n(γђB0/2kT)
where g is the gyromagnetic ratio (42.576 Mhz/T for Hydrogen), h is Planck's constant (6.626068 × 10-34 m2 kg / s) and B0 is the field strength (e.g., 1.5T). Thus, for a 1.5T scanner, the number of measured spins in a 2mm^3 voxel is 1.3137e+15.
(Matlab code: 2.6585e+20*(42.576*1e6*6.6261e-34*1.5/(2*1.3805e-23*310.15))

Implementation
Overview of the package:
The MR Diffusion Simulator is a code written with CUDA programming model to exploit the power of GPUs to accelerate the simulation i.e. for running the simulation on CUDA enabled Nvidia graphics cards. However the code also has the provision to run the same simulation on CPUs which do not have Nvidia graphics cards, but must have the NVCC compiler installed (NOTE: Separate code exists to execute the particle interaction and computation on the CPU hence the simulation does not run on device emulation mode).

Code Overview:
The simulation is to model the motion of water molecules in the presence of neuronal fibers and model the spin evolution for the water molecules when a magnetic gradient is applied from which the relative magnetic gradient would be computed. The anisotropy in the motion (this simulated BOLD response) would be instrumental in understanding how the fibers are oriented.
The existing CUDA example code for “particles” has been adopted in developing our simulation. Hence most of the object oriented framework and graphics functions remain very similar to the CUDA sdk example. The simulation is instantiated in 'diffusion.cpp' which also contains all the visualization modules to render the simulation. The other main modules are a) 'particleSystem' - contains the variable and functions that support the simulation and b) 'particles_kernel' (.cu is the GPU version and Cpu.cpp the corresponding CPU version) – contains the function that performs the actual computation modeling the motion of the molecules.

Detailed code walk through:
The heart of the simulation is to find the new position of the molecule every time step. The presence of the neuronal fibers affect the perfectly random motion of the water molecules. This interaction is to be accounted for while computing the new position of the molecule. It is however important to identify all the possible fibers with which the molecule could potentially interact with each random step taken. If not done carefully this could be the major source of overhead and the simulation would become ridiculously memory bound.

Figure 1: Space grid into cubes
As a result of the above mentioned notion, the space is grid into cubes such that each cube holds the information of the fiber that it contains. The cube to which the particle belongs to is to be identifies so that only those fibers need be retrieved to compute the new position (i.e. its interaction only with the fibers in the vicinity). A list is first created which holds the indices to the tubes that are present in the given cube in the space.

        Figure 2: (a), (b) Scenarios to illustrate the molecule-fiber interaction
Hence during simulation the particles position is used to determine which cube the particle currently resides (this index gives the starting location of the cube level list which holds the indices to the tube list which contains the tube positions and their radii) :-
cubePos.x = (pos.x – worldOrigin.x ) / cubeSize
cubeListIndex = cubePos.z x gridSize.y x gridSize.x + cubePos.y x gridSize.x +	cubePos.x
However, as depicted by Figure 2 (b) it is not enough to only consider the cube in which the molecule resides but also its neighboring cubes for accurate simulation.
The main simulation kernel executes as follows:
1. First compute the new position as a random step taken
2. Find if the new position is valid as restricted by the presence of neighboring fibers and governed by the permeability of the medium [curDis/preDis - distance of position of molecule to center of fiber]
  1. If curDis <= radius && prevDis > radius – the particle is trying to move from outside to inside of the fiber
  2. If curDis > radius && prevDis <= radius – the particle is trying to move from inside to outside of the fiber
  3. Final position : either bounce back or remain in the new calculated position, determined by the permeability
In a more realistic situation the packing of the fibers will be so dense that there would potentially be more molecules residing inside a fiber at a given instant of time than outside to the extent that keeping track of the tubes within which it resides would obviate the need to consider all the other fibers in the vicinity.

(a)

(b)

        Figure 3: Illustration of another optimization
Yet another optimization in order to reduce the number of fibers to be considered for each molecule, that was incorporated was to consider only those fibers from the neighboring cubes which lie within 1.5 times the maximum radius of the fibers present in the space. This would yield accurate results under the assumption that the step size for the motion of the molecule is much smaller than the radius of the fiber.

GPU Specific Optimization :
1. The first optimization made was to pin the list containing the position & radius of each fiber to texture memory and retrieve them through texture fetches
2. The other optimization incorporated was an effort to support DMA coalescing by sorting the particles based on there new position in the space so that access pattern of the tube positions by threads of molecules close in the space would support DMA coalescing.